## Slide 1: Fuzzy Congestion Control using AQM in WSN
Comparison of 12 Research Papers
Final Year Project Presentation

## Slide 2: 📌 Most common inputs: Queue length (avg/instant), packet loss; sometimes channel load & packet priority 📌 Placement of fuzzy AQM: Mostly at cluster-heads/gateways or every forwarding node (hop-by-hop) 📌 Typical outputs: Drop/mark probability (AQM), explicit congestion notification, rate adjustment 📌 Evaluation metrics: Packet delivery ratio, delay, packet loss, energy; mostly simulation-based

## Slide 3: Comparison of 12 Papers
Paper | Year | Inputs | Node Role | Output (Action) | Result
Rezaee & Pasandideh | 2017 | Qlen, channel load, priority | Cluster-heads | Drop prob + ECN | Reduced loss, delay
Aimtongkham et al. | 2018 | Qlen, arrival, loss | Node-level | Predict + early drop | Better throughput
FLACC | 2019 | AQL, PL | Forwarding nodes | Drop prob | Outperforms RED
FBACC variants | 2013–15 | Qlen, arrival rate | Node-level | Early drop + rate ctrl | Reduced loss & delay
Chakraborty (Trust) | 2013 | Qlen, trust, loss | Node-level | Rate adjust + drop | Trust + congestion
Lin (Fuzzy-PID) | 2020 | Qlen, loss rate | Gateways | PID+fuzzy ctrl | Smooth stable control
Abu-Shareha (AQM) | 2023 | Qlen, traffic desc. | Routers | Drop prob (fuzzy GA) | Optimized AQM tuning
Mazloomi (Hybrid) | 2024 | Qlen, link, pred. | Cluster-heads | Fuzzy+SVR | Energy-efficient
Sonmez (WMSN) | 2014 | Qlen, delay, priority | Gateways | Prioritize frames | Preserves QoS
Hatamian et al. | 2015–17 | Load, neighbors | Routing nodes | Rate adjust + route | Avoids hotspots
IFCCDC | 2012 | Qlen, channel cond. | Node-level | Detect + drop | Reduced drops
Rajeswari | 2022 | Qlen, delay, loss | Cluster-heads | Type-2 fuzzy drop | QoS under uncertainty

## Slide 4: ✅ Strengths: Adaptive decision-making, smooth congestion handling, supports priority data ✅ Several protocols outperform traditional RED/GRED in delay and packet loss ⚠️ Weaknesses: Simulation-heavy, limited real-world mote tests, computational overhead at CHs ⚠️ Parameter tuning (membership functions, fuzzy rules) still manual in most works 👉 Future: Use adaptive fuzzy sets, hybrid fuzzy+ML, hardware energy profiling